## Slide 1
SAIL PERFORMANCE OVERVIEW

## Slide 2: SAIL Performance : Sep’26 & Apr-Sep’26
 | Annual Cap. | Sep'26 |  |  |  | Apr-Sep'26 |  |  | 
Plant |  | APP | Actual | % Growth Over Sep’25 | % CU | APP | Actual | % Growth Over CPLY | % CU
Hot Metal | 21113 | 1945 | 1594 | -1 | 92 | 11286 | 10203 | 2 | 96
Crude Steel | 19946 | 1896 | 1492 | -1 | 91 | 10967 | 9605 | 1 | 96
Finished Steel | 17500 | 1546 | 1328 | -2 | 92 | 9230 | 8156 | 1 | 93
Saleable Steel | 19190 | 1762 | 1495 | -5 | 95 | 10343 | 9406 | -2 | 98
Figures in ‘000 Tones
H-1 Highlights | SAIL achieved best ever H1 (Apr-Sep) 2026-27 production for following:- Hot Metal 10.203 MT (Previous best 10.135 MT in H1 2023-24) Crude Steel 9.605 MT (Previous best 9.505 MT in H1 2025-26) Finished Steel 8.389 MT (Previous best 8.301 MT in H1 2025-26)

## Slide 3: SAIL Plant-wise Performance : Sep’26 & Apr-Sep’26
Hot Metal |  |  |  |  |  |  |  |  | 
Plant | Annual Cap. | Sep'26 |  |  |  | Apr-Sep'26 |  |  | 
Plant |  | APP | Actual | % Growth Over Sep’25 | % CU | APP | Actual | % Growth Over CPLY | % CU
BSP | 6275 | 542 | 370 | -21 | 72 | 3287 | 2997 | 2 | 95
DSP | 2450 | 229 | 205 | 6 | 102 | 1255 | 1146 | -3 | 93
RSP | 4438 | 453 | 371 | 2 | 102 | 2556 | 2154 | 0 | 97
BSL | 5250 | 465 | 411 | 21 | 95 | 2756 | 2539 | 13 | 96
ISP | 2700 | 256 | 237 | -3 | 107 | 1432 | 1366 | -9 | 101
Total | 21113 | 1945 | 1594 | -1 | 92 | 11286 | 10203 | 2 | 96
Crude Steel |  |  |  |  |  |  |  |  | 
Plant | Annual Cap. | Sep'26 |  |  |  | Apr-Sep'26 |  |  | 
Plant |  | APP | Actual | % Growth Over Sep’25 | % CU | APP | Actual | % Growth Over CPLY | % CU
BSP | 5961 | 530 | 355 | -21 | 72 | 3212 | 2866 | 1 | 96
DSP | 2200 | 212 | 182 | 0 | 101 | 1158 | 1027 | -6 | 93
RSP | 4216 | 435 | 342 | 3 | 99 | 2441 | 2002 | 0 | 95
BSL | 4655 | 447 | 372 | 24 | 97 | 2636 | 2302 | 13 | 99
ISP | 2500 | 241 | 223 | -1 | 109 | 1341 | 1281 | -9 | 102
SSPs | 414 | 31 | 17 | -9 | 49 | 179 | 128 | -10 | 62
Total | 19946 | 1896 | 1492 | -1 | 91 | 10967 | 9605 | 1 | 96
Figures in ‘000 Tones

## Slide 4: Major Breakdowns/Delays during Sep’26 & Apr-Sep’26
HM & CS | BSP (Sep’26): BF#4: BLT chute changing & revival-15 days BF#7: Multiple slipping & revival- 3 days BF#8: HBV of Stove#2 & BLT chute changing (5+3 days) DSP(Apr-Sep’26): BF-2: Extended CR (Took 14 days more than Plan of 45 days, Apr-Jun’26) & Extended stabilisation after CR (Took 10 days) BF-3, 4: Shutdown in view of SMS Flare stack repair job (48 Hrs each, Apr’26) ISP(Sep’26): Restricted sinter production due to wet & sticky Raw Materails ISP (Apr-Sep’26): Extended CR of BF-5 (Plan: 10 days, Actual: 13 days, May’26) ASP: EAF-3: Transformer oil leakage (25 days, Apr-May’26), Foundation breakdown in tapping car (52 days, Jun-Jul’26) EAF-2: Foundation work of tapping Car from 07.8.26- cont.

## Slide 5: SAIL Plant-wise Performance : Sep’26 & Apr-Sep’26
Saleable Steel |  |  |  |  |  |  |  |  | 
Plant | Annual Cap. | Sep'26 |  |  |  | Apr-Sep'26 |  |  | 
Plant |  | APP | Actual | % Growth Over Sep’25 | % CU | APP | Actual | % Growth Over CPLY | % CU
BSP | 5560 | 495 | 384 | -13 | 84 | 2926 | 2687 | 0 | 96
DSP | 2120 | 204 | 170 | 1 | 97 | 1108 | 964 | -8 | 91
RSP | 4306 | 370 | 333 | -4 | 94 | 2334 | 2086 | 2 | 97
BSL | 4240 | 416 | 355 | -5 | 102 | 2423 | 2257 | 1 | 106
ISP | 2390 | 232 | 221 | -1 | 113 | 1290 | 1229 | -8 | 103
SSPs | 574 | 45 | 32 | 16 | 67 | 262 | 183 | 1 | 63
Total | 19190 | 1762 | 1495 | -5 | 95 | 10343 | 9406 | -2 | 98
Finished Steel |  |  |  |  |  |  |  |  | 
Plant | Annual Cap. | Sep'26 |  |  |  | Apr-Sep'26 |  |  | 
Plant |  | APP | Actual | % Growth Over Sep’25 | % CU | APP | Actual | % Growth Over CPLY | % CU
BSP | 4900 | 450 | 374 | -5 | 93 | 2718 | 2401 | 3 | 98
DSP | 1392 | 116 | 84 | -6 | 73 | 680 | 539 | -8 | 77
RSP | 4306 | 370 | 333 | -4 | 94 | 2334 | 2086 | 2 | 97
BSL | 4200 | 376 | 347 | 1 | 101 | 2160 | 2069 | 4 | 98
ISP | 2300 | 200 | 170 | 1 | 90 | 1144 | 946 | -7 | 82
SSPs | 402 | 34 | 20 | 27 | 61 | 194 | 116 | -3 | 58
Total | 17500 | 1546 | 1376 | -1 | 96 | 9230 | 8389 | 1 | 96
Figures in ‘000 Tones

## Slide 6: Major Breakdowns/Delays during Sep’26 & Apr-Sep’26
Figures in ‘000 Tones
FS | BSP (Sep’26): RSM: CR from 19th Sept26- Contd MM, WRM, BRM : Input Billet / BF Gas constraints Plate Mill: 2 RHFs operation for 11 days (Repair of RHF-1&3) DSP(Apr-Sep’26): MSM: Extended CR (Plan: 6 days, Actual: 8 days, Apr’26) M Mill: Extended CR (Plan: 10 days, Actual: 13 days, Apr-May’26) RSP(Sep’26): HSM-2 : Single RHF operation for 6.5 days (roof brick fallen) ISP (Apr-Sep’26): WRM: Extended CR (Plan: 10 days, Actual: 13 days in May’26) Bar Mill: Extended CR (Plan: 11 days, Actual: 17 days in May’26) USM: Extended CR (Plan: 11 days, Actual: 22 days in May’26) VISL: Roof sheeting job (15 days, Apr-May’26) & RHF down for arch & roof bricks fallen (44 days, May-Jun’26)

## Slide 7: SAIL Techno Performance (Apr-Sep’26)
Chart: Coke Rate (kg/THM)
| FY25 | FY26 | FY'27 Target | Sep | Apr-Sep
Series 1 | 421 | 419 | 400 | 432 | 424
Chart: PCI Rate (kg/THM)
| FY25 | FY26 | FY'27 Target | Sep | Apr-Sep
Series 1 | 113 | 113 | 119 | 99 | 110
Chart: BF Productivity (T/m3/Day )
| FY25 | FY26 | FY'27 Target | Sep | Apr-Sep
Series 1 | 2.02 | 2.09 | 2.24 | 1.91 | 2.04
Chart: Sp. Energy (Gcal/TCS )
| FY25 | FY26 | FY'27 Target | Sep | Apr-Sep
Series 1 | 6.26 | 6.18 | 6.03 | 6.41 | 6.23
Chart: Sp. CO2 Emission (T/TCS )
| FY25 | FY26 | FY'27 Target | Aug | Apr-Aug
Series 1 | 2.55 | 2.53 | 2.43 | 2.59 | 2.6
Good
Good
Good
Good
Good
Chart: Fuel Rate (kg/THM)
| FY25 | FY26 | FY 27 Target | Sep | Apr-Sep
Series 1 | 558 | 553 | 536 | 551 | 554
Good

## Slide 8: BSP Performance : Sep’26 & Apr-Sep’26
 | Annual Cap. | Sep'26 |  |  |  | Apr-Sep'26 |  |  | 
Plant |  | APP | Actual | % Growth Over Sep’25 | % CU | APP | Actual | % Growth Over CPLY | % CU
Hot Metal | 6275 | 542 | 370 | -21 | 72 | 3287 | 2997 | 2 | 95
Crude Steel | 5961 | 530 | 355 | -21 | 72 | 3212 | 2866 | 1 | 96
Finished Steel | 4900 | 450 | 374 | -5 | 93 | 2718 | 2401 | 3 | 98
Saleable Steel | 5560 | 495 | 384 | -13 | 84 | 2926 | 2687 | 0 | 96
Figures in ‘000 Tones
Highlights | BSP achieved best H1 (Apr-Sep) 2026-27 production for following:- Hot Metal 2.997 MT (Previous best 2.983 MT in H1 2023-24) Crude Steel 2.866 MT (Previous best 2.833 MT in H1 2025-26) Finished Steel 2.401 MT (Previous best 2.327 MT in H1 2025-26)

## Slide 9: BSP Techno Performance
Chart: Coke Rate (kg/THM)
| FY25 | FY26 | FY'27 Target | Sep | Apr-Sep
Series 1 | 430 | 426 | 407 | 447 | 432
Chart: PCI Rate (kg/THM)
| FY25 | FY26 | FY'27 Target | Sep | Apr-Sep
Series 1 | 134 | 118 | 125 | 99 | 114
Chart: BF Productivity (T/m3/Day )
| FY25 | FY26 | FY'27 Target | Sep | Apr-Sep
Series 1 | 1.93 | 2.04 | 2.24 | 1.79 | 2.03
Chart: Sp. Energy (Gcal/TCS )
| FY25 | FY26 | FY'27 Target | Sep | Apr-Sep
Series 1 | 6.3 | 6.08 | 5.86 | 6.92 | 6.19
Chart: Sp. CO2 Emission (T/TCS )
| FY25 | FY26 | FY'27 Target | Aug | Apr-Aug
Series 1 | 2.62 | 2.54 | 2.45 | 2.6 | 2.54
Good
Good
Good
Good
Good
Chart: Fuel Rate (kg/THM)
| FY25 | FY26 | FY 27 Target | Sep | Apr-Sep
Series 1 | 585 | 566 | 550 | 566 | 566
Good

## Slide 10: DSP Performance : Sep’26 & Apr-Sep’26
 | Annual Cap. | Sep'26 |  |  |  | Apr-Sep'26 |  |  | 
Plant |  | APP | Actual | % Growth Over Sep’25 | % CU | APP | Actual | % Growth Over CPLY | % CU
Hot Metal | 2450 | 229 | 205 | 6 | 102 | 1255 | 1146 | -3 | 93
Crude Steel | 2200 | 212 | 182 | 0 | 101 | 1158 | 1027 | -6 | 93
Finished Steel | 1392 | 116 | 84 | -6 | 73 | 680 | 539 | -8 | 77
Saleable Steel | 2120 | 204 | 170 | 1 | 97 | 1108 | 964 | -8 | 91
Figures in ‘000 Tones

## Slide 11: DSP Techno Performance
Chart: Coke Rate (kg/THM)
| FY25 | FY26 | FY'27 Target | Sep | Apr-Sep
Series 1 | 456 | 463 | 440 | 455 | 451
Chart: PCI Rate (kg/THM)
| FY25 | FY26 | FY'27 Target | Sep | Apr-Sep
Series 1 | 65 | 60 | 77 | 72 | 69
Chart: BF Productivity (T/m3/Day )
| FY25 | FY26 | FY'27 Target | Sep | Apr-Sep
Series 1 | 1.79 | 1.74 | 1.96 | 1.77 | 1.83
Chart: Sp. Energy (Gcal/TCS )
| FY25 | FY26 | FY'27 Target | Sep | Apr-Sep
Series 1 | 6.35 | 6.36 | 6.34 | 6.47 | 6.46
Chart: Sp. CO2 Emission (T/TCS )
| FY25 | FY26 | FY'27 Target | Aug | Apr-Aug
Series 1 | 2.48 | 2.52 | 2.48 | 2.6 | 2.64
Good
Good
Good
Good
Good
Chart: Fuel Rate (kg/THM)
| FY25 | FY26 | FY 27 Target | Sep | Apr-Sep
Series 1 | 543 | 546 | 535 | 541 | 539
Good

## Slide 12: RSP Performance : Sep’26 & Apr-Sep’26
 | Annual Cap. | Sep'26 |  |  |  | Apr-Sep'26 |  |  | 
Plant |  | APP | Actual | % Growth Over Sep’25 | % CU | APP | Actual | % Growth Over CPLY | % CU
Hot Metal | 4438 | 453 | 371 | 2 | 102 | 2556 | 2154 | 0 | 97
Crude Steel | 4216 | 435 | 342 | 3 | 99 | 2441 | 2002 | 0 | 95
Finished Steel | 4306 | 370 | 333 | -4 | 94 | 2334 | 2086 | 2 | 97
Saleable Steel | 4306 | 370 | 333 | -4 | 94 | 2334 | 2086 | 2 | 97
Figures in ‘000 Tones

## Slide 13: RSP Techno Performance
Chart: Coke Rate (kg/THM)
| FY25 | FY26 | FY'27 Target | Sep | Apr-Sep
Series 1 | 391 | 386 | 381 | 410 | 402
Chart: PCI Rate (kg/THM)
| FY25 | FY26 | FY'27 Target | Sep | Apr-Sep
Series 1 | 133 | 143 | 137 | 134 | 141
Chart: BF Productivity (T/m3/Day )
| FY25 | FY26 | FY'27 Target | Sep | Apr-Sep
Series 1 | 2.31 | 2.46 | 2.51 | 1.97 | 2.22
Chart: Sp. Energy (Gcal/TCS )
| FY25 | FY26 | FY'27 Target | Sep | Apr-Sep
Series 1 | 5.92 | 6 | 5.98 | 6.13 | 6.1
Chart: Sp. CO2 Emission (T/TCS )
| FY25 | FY26 | FY'27 Target | Aug | Apr-Aug
Series 1 | 2.53 | 2.51 | 2.41 | 2.6 | 2.61
Good
Good
Good
Good
Good
Chart: Fuel Rate (kg/THM)
| FY25 | FY26 | FY 27 Target | Sep | Apr-Sep
Series 1 | 549 | 547 | 528 | 560 | 559
Good

## Slide 14: BSL Performance : Sep’26 & Apr-Sep’26
 | Annual Cap. | Sep'26 |  |  |  | Apr-Sep'26 |  |  | 
Plant |  | APP | Actual | % Growth Over Sep’25 | % CU | APP | Actual | % Growth Over CPLY | % CU
Hot Metal | 5250 | 465 | 411 | 21 | 95 | 2756 | 2539 | 13 | 96
Crude Steel | 4655 | 447 | 372 | 24 | 97 | 2636 | 2302 | 13 | 99
Finished Steel | 4200 | 376 | 347 | 1 | 101 | 2160 | 2069 | 4 | 98
Saleable Steel | 4240 | 416 | 355 | -5 | 102 | 2423 | 2257 | 1 | 106
Figures in ‘000 Tones
Highlights | BSL achieved best H1 (Apr-Sep) 2026-27 production for following:- Hot Metal 2.539 MT (Previous best 2.477 MT in H1 2024-25) Crude Steel 2.302 MT (Previous best 2.213 MT in H1 2024-25) Saleable Steel 2.257 MT (Previous best 2.244 MT in H1 2025-26) Finished Steel 2.069 MT (Previous best 1.996 MT in H1 2025-26)

## Slide 15: BSL Techno Performance
Chart: Coke Rate (kg/THM)
| FY25 | FY26 | FY'27 Target | Sep | Apr-Sep
Series 1 | 445 | 446 | 420 | 459 | 449
Chart: PCI Rate (kg/THM)
| FY25 | FY26 | FY'27 Target | Sep | Apr-Sep
Series 1 | 85 | 89 | 100 | 69 | 87
Chart: BF Productivity (T/m3/Day )
| FY25 | FY26 | FY'27 Target | Sep | Apr-Sep
Series 1 | 1.91 | 1.97 | 2.1 | 1.88 | 1.91
Chart: Sp. Energy (Gcal/TCS )
| FY25 | FY26 | FY'27 Target | Sep | Apr-Sep
Series 1 | 6.52 | 6.44 | 6.2 | 6.32 | 6.33
Chart: Sp. CO2 Emission (T/TCS )
| FY25 | FY26 | FY'27 Target | Aug | Apr-Aug
Series 1 | 2.62 | 2.6 | 2.47 | 2.57 | 2.61
Good
Good
Good
Good
Good
Chart: Fuel Rate (kg/THM)
| FY25 | FY26 | FY 27 Target | Sep | Apr-Sep
Series 1 | 548 | 551 | 535 | 541 | 549
Good

## Slide 16: ISP Performance : Sep’26 & Apr-Sep’26
 | Annual Cap. | Sep'26 |  |  |  | Apr-Sep'26 |  |  | 
Plant |  | APP | Actual | % Growth Over Sep’25 | % CU | APP | Actual | % Growth Over CPLY | % CU
Hot Metal | 2700 | 256 | 237 | -3 | 107 | 1432 | 1366 | -9 | 101
Crude Steel | 2500 | 241 | 223 | -1 | 109 | 1341 | 1281 | -9 | 102
Finished Steel | 2300 | 200 | 170 | 1 | 90 | 1144 | 946 | -7 | 82
Saleable Steel | 2390 | 232 | 221 | -1 | 113 | 1290 | 1229 | -8 | 103
Figures in ‘000 Tones

## Slide 17: ISP Techno Performance
Chart: Coke Rate (kg/THM)
| FY25 | FY26 | FY'27 Target | Sep | Apr-Sep
Series 1 | 372 | 373 | 348 | 376 | 374
Chart: PCI Rate (kg/THM)
| FY25 | FY26 | FY'27 Target | Sep | Apr-Sep
Series 1 | 134 | 136 | 150 | 123 | 132
Chart: BF Productivity (T/m3/Day )
| FY25 | FY26 | FY'27 Target | Sep | Apr-Sep
Series 1 | 2.27 | 2.32 | 2.47 | 2.29 | 2.31
Chart: Sp. Energy (Gcal/TCS )
| FY25 | FY26 | FY'27 Target | Sep | Apr-Sep
Series 1 | 6.16 | 6.09 | 5.89 | 6.14 | 6.16
Chart: Sp. CO2 Emission (T/TCS )
| FY25 | FY26 | FY'27 Target | Aug | Apr-Aug
Series 1 | 2.36 | 2.41 | 2.27 | 2.58 | 2.67
Good
Good
Good
Good
Good
Chart: Fuel Rate (kg/THM)
| FY25 | FY26 | FY 27 Target | Sep | Apr-Sep
Series 1 | 546 | 543 | 525 | 540 | 542
Good

## Slide 19
Plant | Apr-Sep’26 | Apr-Sep’25
BSP | SMS2 Conv A (62 days in Jun-Aug’26) SMS2 Conv B (14 days in June'26) SMS-2 Conv.C (11 days in Apr’26) SMS-3 Conv.2 (12 days in Aug’26) SMS-3 Conv.3 (11 days in Apr’26) SMS-3 CK-1 ( 8 days in Apr’26) SMS-3 CK-2 ( 7 days in Aug’26) SMS-3 CV-1 ( 8 days in Sep’26) RSM (19.9.26-cont.) URM (7 days in May’26) WRM (13 days in Apr’26) P Mill (6 days in Jun’26) M Mill (7 days in Jul’26) BRM (8 days in Aug’26) | BF-8 (3 days in Jul’25) SMS-2 Conv.C (18 days in Apr-May’25 ) SMS-3 Conv.1 (12 days in Apr’25) SMS-3 Conv 2 (13 days in Jul’25) RSM (2 days in May’25 + 8 days in Jun’25) URM (7 days in Jul’25) P Mill (13 days in Apr-May’25)
DSP | BF-2 (60 days in Apr-Jun’26) SMS Conv.2 (23 days in Apr-May’26) SMS Conv. 3 (11 days in Jun’26) BRC (9 days.in Apr-May’26) MM ( 13 days in Apr-May’26) MSM (8 days in Apr’26) | BF-4 (2 days in May’25 + 12 days in Jun’25) SMS Conv. - 3 (17 days in May’25) MM (9 days in Apr’25) WAP (11 days in May’25)
Major Capital Repairs

## Slide 20
Plant | Apr-Aug’26 | Apr-Aug’25
RSP | SMS-1 LD-P (10 days in Jun-Jul’26) SMS-1 LD-Q (6 days in Apr’26 SMS-2 Conv.B (17 days in May'26) SMS-2 Caster-1 (7 days in June'26) NPM (11 days in Jul’26) HSM-2 (10 days in May’26) | BF-5 (5 days in Jul’25) SMS-1 LD-Q (14 days in Jun’25) SMS-2 Conv A (7 days in Jul’25) SMS-2 Conv.B (14 days in May’25) SMS-2 Caster-2 (7 days) HSM-2: 6 days in Jul’25
BSL | BF-1 (4 days in Aug’26) BF-4 (8 days in Jul’26) SMS-1 Conv. D (25 days in May’26) SMS-2 Conv2 (13 days in Jul’26) HSM (8 days in May’26) | BF-1 (11 days in Apr’25) BF-4 (4 days in Jun’25) SMS-1 Conv. D (11 days in May’25) SMS-1 Conv. E (17 days in Jun-Jul’25)
ISP | BF-5 (13 days in May'26) WRM (13 days in May'26) Bar Mill (17 days in May'26) USM (22 days in May'26) | Conv 2 (12 days in Apr-May’25)
Major Capital Repairs

## Slide 21: BSP: Major Breakdowns/Delays during Sep’26
BFs | BF#4: BLT chute changing & revival-15 days BF#7: Multiple slipping & revival- 3 days BF#8: HBV of Stove#2 & BLT chute changing (5+3 days)
Mills | RSM: CR from 19th Sept26- Contd MM, WRM, BRM : Input Billet / BF Gas constraints Plate Mill: 2 RHFs operation for 11 days (Repair of RHF-1&3

## Slide 22: DSP: Major Breakdowns/Delays during Apr-26 & Apr-Sep’26
BFs | Sep’26: MSM: Regular Operational & Mechanical Issues Apr-Sep’26: BF-2: Extended CR (Took 14 days more than Plan of 45 days, Apr-Jun’26) & Extended stabilisation after CR (Took 10 days) BF-3, 4: Shutdown in view of SMS Flare stack repair job (48 Hrs each, Apr’26)
SMS | Shop Shutdown for Flare Stack Repair (48 Hrs during Apr’26)
Mills | MSM: Extended CR (Plan: 6 days, Actual: 8 days, Apr’26) M Mill: Extended CR (Plan: 10 days, Actual: 13 days, Apr-May’26)

## Slide 23: RSP: Major Breakdowns/Delays during Sep’26
Mills | HSM-2 : Single RHF operation for 6.5 days (roof brick fallen)

## Slide 24: ISP: Major Breakdowns/Delays during Sep’26 & Apr-Sep’26
BF | Sep’26: Restricted sinter production due to wet & sticky Raw Materails Apr-Sep’26: Extended CR of BF-5 (Plan: 10 days, Actual: 13 days, May’26)
SMS | BOF-3: Failure of Non-drive end bearing of Tilting mechanism (10 days, Jul’26)
Mills | WRM: Extended CR (Plan: 10 days, Actual: 13 days in May’26) Bar Mill: Extended CR (Plan: 11 days, Actual: 17 days in May’26) USM: Extended CR (Plan: 11 days, Actual: 22 days in May’26)

## Slide 25: SAIL Techno Performance
Chart: Coke Rate (kg/THM)
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 421 | 419 | 400 | 421 | 425 | 415 | 425 | 426 | 432
Chart: PCI Rate (kg/THM)
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 113 | 113 | 119 | 112 | 114 | 116 | 113 | 107 | 99
Chart: BF Productivity (T/m3/Day )
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 2.02 | 2.09 | 2.24 | 2.16 | 2.06 | 2.17 | 2.05 | 1.94 | 1.91
Chart: Sp. Energy (Gcal/TCS )
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 6.26 | 6.18 | 6.03 | 6.17 | 6.3 | 6.14 | 6.19 | 6.2 | 6.41
Chart: Sp. CO2 Emission (T/TCS )
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug
Series 1 | 2.55 | 2.53 | 2.43 | 2.63 | 2.61 | 2.56 | 2.56 | 2.59
Good
Good
Good
Good
Good
Chart: Fuel Rate (kg/THM)
| FY25 | FY26 | FY 27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 558 | 553 | 536 | 554 | 557 | 550 | 557 | 553 | 551
Good

## Slide 26: BSP Techno Performance
Chart: Coke Rate (kg/THM)
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 430 | 426 | 407 | 433 | 429 | 424 | 430 | 432 | 447
Chart: PCI Rate (kg/THM)
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 134 | 118 | 125 | 113 | 118 | 120 | 115 | 112 | 99
Chart: BF Productivity (T/m3/Day )
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 1.93 | 2.04 | 2.24 | 2.1 | 2.08 | 2.11 | 2.09 | 1.96 | 1.79
Chart: Sp. Energy (Gcal/TCS )
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 6.3 | 6.08 | 5.86 | 6.03 | 6.04 | 6.03 | 6.06 | 6.26 | 6.92
Chart: Sp. CO2 Emission (T/TCS )
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug
Series 1 | 2.62 | 2.54 | 2.45 | 2.58 | 2.52 | 2.5 | 2.51 | 2.6
Good
Good
Good
Good
Good
Chart: Fuel Rate (kg/THM)
| FY25 | FY26 | FY 27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 585 | 566 | 550 | 569 | 567 | 564 | 565 | 564 | 566
Good

## Slide 27: DSP Techno Performance
Chart: Coke Rate (kg/THM)
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 456 | 463 | 440 | 453 | 452 | 453 | 446 | 451 | 455
Chart: PCI Rate (kg/THM)
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 65 | 60 | 77 | 63 | 71 | 66 | 71 | 71 | 72
Chart: BF Productivity (T/m3/Day )
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 1.79 | 1.74 | 1.96 | 1.85 | 1.83 | 1.79 | 1.89 | 1.84 | 1.77
Chart: Sp. Energy (Gcal/TCS )
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 6.35 | 6.36 | 6.34 | 6.38 | 6.56 | 6.44 | 6.41 | 6.53 | 6.47
Chart: Sp. CO2 Emission (T/TCS )
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug
Series 1 | 2.48 | 2.52 | 2.48 | 3.02 | 2.59 | 2.58 | 2.5 | 2.6
Good
Good
Good
Good
Good
Chart: Fuel Rate (kg/THM)
| FY25 | FY26 | FY 27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 543 | 546 | 535 | 539 | 542 | 539 | 537 | 537 | 541
Good

## Slide 28: RSP Techno Performance
Chart: Coke Rate (kg/THM)
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 391 | 386 | 381 | 392 | 396 | 390 | 407 | 416 | 410
Chart: PCI Rate (kg/THM)
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 133 | 143 | 137 | 145 | 147 | 144 | 142 | 135 | 134
Chart: BF Productivity (T/m3/Day )
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 2.31 | 2.46 | 2.51 | 2.5 | 2.39 | 2.46 | 2.29 | 1.89 | 1.97
Chart: Sp. Energy (Gcal/TCS )
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 5.92 | 6 | 5.98 | 6.15 | 6.22 | 5.98 | 6.12 | 6 | 6.13
Chart: Sp. CO2 Emission (T/TCS )
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug
Series 1 | 2.53 | 2.51 | 2.41 | 2.61 | 2.63 | 2.58 | 2.62 | 2.6
Good
Good
Good
Good
Good
Chart: Fuel Rate (kg/THM)
| FY25 | FY26 | FY 27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 549 | 547 | 528 | 553 | 559 | 551 | 566 | 565 | 560
Good

## Slide 29: BSL Techno Performance
Chart: Coke Rate (kg/THM)
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 445 | 446 | 420 | 441 | 437 | 438 | 459 | 447 | 459
Chart: PCI Rate (kg/THM)
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 85 | 89 | 100 | 93 | 100 | 95 | 88 | 77 | 69
Chart: BF Productivity (T/m3/Day )
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 1.91 | 1.97 | 2.1 | 2.07 | 1.94 | 2.06 | 1.77 | 1.79 | 1.88
Chart: Sp. Energy (Gcal/TCS )
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 6.52 | 6.44 | 6.2 | 6.32 | 6.35 | 6.35 | 6.38 | 6.29 | 6.32
Chart: Sp. CO2 Emission (T/TCS )
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug
Series 1 | 2.62 | 2.6 | 2.47 | 2.58 | 2.62 | 2.6 | 2.58 | 2.57
Good
Good
Good
Good
Good
Chart: Fuel Rate (kg/THM)
| FY25 | FY26 | FY 27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 548 | 551 | 535 | 549 | 551 | 543 | 557 | 542 | 541
Good

## Slide 30: ISP Techno Performance
Chart: Coke Rate (kg/THM)
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 372 | 373 | 348 | 384 | 415 | 361 | 368 | 368 | 376
Chart: PCI Rate (kg/THM)
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 134 | 136 | 150 | 125 | 93 | 142 | 144 | 140 | 123
Chart: BF Productivity (T/m3/Day )
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 2.27 | 2.32 | 2.47 | 2.26 | 1.83 | 2.48 | 2.41 | 2.41 | 2.29
Chart: Sp. Energy (Gcal/TCS )
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 6.16 | 6.09 | 5.89 | 6.11 | 7.32 | 6.02 | 6.09 | 5.97 | 6.14
Chart: Sp. CO2 Emission (T/TCS )
| FY25 | FY26 | FY'27 Target | Apr | May | Jun | Jul | Aug
Series 1 | 2.36 | 2.41 | 2.27 | 2.62 | 2.98 | 2.59 | 2.65 | 2.58
Good
Good
Good
Good
Good
Chart: Fuel Rate (kg/THM)
| FY25 | FY26 | FY 27 Target | Apr | May | Jun | Jul | Aug | Sep
Series 1 | 546 | 543 | 525 | 540 | 542 | 538 | 549 | 543 | 540
Good